Silver Shadow alternate parts:

-Carburetors: Skinners Union (SU) Carburetors are used. Needle & Seats, Jets, Gasket Packs. etc.. all available from SU suppliers. 
-Engine Oil Filter: Crossland Type 345 (or F3750), from Nemac Distributing Ltdl, Gormley, Ontario. 1-800-668-7522, or R&S European Car parts at about $15.99 
-Transmission: Transmission is the GM Turbo Hydra-Matic 400 made by Allison with Rolls-Royce custom modifications. The Hydra-Matic 400 was used on 1972/79 AMC-Jeeps., and 1967/84 Cadillacs, etc. Parts can be obtained from any GM dealer. 
-Early Shadow Bypass Hose: Gates 19219, cut off 3/4" diameter portion and it's a perfect fit with moulded curve. This is the one from the pipe attached to the t-stat housing bolt (water pump) to overflow tank above radiator 1966-? 
-Power Steering/ACC Fan Belt: Silver Shadow & Shadow II cars from 20755, (and possibly Saginaw p/s cars with aircon before them) ACC/Power Steering belts are Gates (US) #7640, or Dayco #15640, or Napa 25-7640 measuring at 1626mm x 11.5mm like original. 11A1625 is the metric part #. Gates industrial SPA 1632 will also work, but actually specs out at 12.7mm (1/2") wide. 
-Power Steering Pump: NAPA Auto Parts 20-840 (OE is GM) 
-Transmission Oil Filter: GM6437741; FRAMFT1020; ACPFI68, Kit: Napa 1-4558 
-Air Filter: (with Carb.) Crossland 9088, F9406 (about $27) 
-Fuel Filter: (Fuel Pump): Crossland 444 (Carburetor): WIX 33051 (w/ valve plate & spring removed) 
-Manual Control Shaft Oil Seal: GM 8657163. 
-Brake Pads: See Spirit/Spur section 
-Front Brake Caliper Rebuild Kits: PBR kit K606S, two kits required, one each side. 
-Fuel Pump: Fuel pump is the SU type AUF-402. The fuel pump is comprised of two individual pumping units each connected to a common central casting which houses the inlet and outlet valves, both pumping units operate simultaneously. This is a unique combination for Rolls-Royce . However, the pumping units and valves are the same as used in the SU type AUF-503 (dual/independent pumps used on 1963/67 Land Rovers), and in the SU type AUF-30 I (two single pumps used on 1963/76 Jaguars).